Centaurus Computing
RIOSocket
Ubiquitous Of Ethernet With Performance Of RapidIO

---
Features
        RIOSocket – Basic
- RapidIO fabric enumeration
- Ethernet emulation over RapidIO fabric using standard TCP/IP stack
- Ability to run standard unmodified Socket library based utilities like sftp, scp, etc on RapidIO fabric
- Ability to run standard communication middlewares like Hadoop or OpenMPI
- Sustained application level throughput measured by standard iperf utility in excess of 14 Gbps.
- Support for 100s of node support
- Support for x86 architecture. Support on other architectures can be added on request basis.
RIOSocket – Advanced
- RapidIO fabric enumeration
- Ethernet emulation over RapidIO fabric using standard TCP/IP stack
- TCP/IP Stack bypass for latency sensitive application achieving sub-two micro second latency.
- Socket Switch to select between the above two transport paths
- Multiple NIC support providing link aggregation and redundancies
- Ethernet fail-safe on RapidIO link failure
- Ability to run standard unmodified Socket library based utilities like sftp, scp, etc on RapidIO fabric
- Ability to run standard communication middlewares like Hadoop or OpenMPI
- Sustained application level throughput measured by standard iperf utility in excess of 14 Gbps
- Application point to point latency of < 1-2 usec for small packet sizes.
- Support for 100s of nodes
- Support of x86 architecture. Support on other architectures can be added on request basis.

---
RIOSocket – 30,000 Feet
Unmodified Socket
Application
RIOSocket-Basic
Socket API
Socket Lib
RIOSocketLib
RIOSocket Kernel Modules
RapidIO
NIC
RapidIO
NIC
TCP/IP

---
RIOSocket-Basic Component Diagram

---
RIOSocket-Basic Packet Path
Node 1
Node 2
Socket Application
Socket Application
TCP/IP
TCP/IP
RIOSocket-Basic NIC
Driver
RIOSocket-Basic NIC
Driver
Packet Size
(sysfs config)
Messaging
Shared Memory
Messaging
DMA

---
RIOSocket-Basic Shared Memory Based Transfer
Node 2
Node 1
RIOSocket NIC Driver
RIOSocket NIC Driver
DMA
TX
memcpy
Rx
Node 3
RIOSocket NIC Driver

---
Shared Memory Packet Transfer – Tx Driver View
Application
Node
Doorbell
Socket Lib
Optimization Note:
We can use multiple
DMA channels
Node
TCP/IP
With MTU is set to 64K
Which enables stack to
Send larger packet and CRC
Is turned off reducing the CPU
Utilization
TX Handler
Doorbell
Node
DMA Controller
Channel 0
Doorbell
SKB
Node
Doorbell
SKB-Node0
SKB-Node1
SKB-Node0
SKB-NodeN
Dynamic
descriptor
appending

---
Shared Memory Packet Transfer – Rx Driver View
Application
Socket Lib
Is there a way to avoid
his mempcy
TCP/IP
RX NAPI-Node0
Memcpy
Shm → Skb
RX NAPI-Node1
Memcpy
Shm → Skb
RX NAPI-Node2
Memcpy
Shm → Skb
RX NAPI-NodeN
Memcpy
Shm → Skb
Doorbell
Doorbell
Doorbell
Doorbell
Shared
Memory
Ring Buffer
Shared
Memory
Ring Buffer
Shared
Memory
Ring Buffer
Shared
Memory
Ring Buffer
NIC

---
Performance
Packet Size vs Throughput
Packet Size
Throughput Mbytes/s